## Slide 1: LiveSync: Deformed Viewing Spheres for Knowledge-Based Navigation
Peter Kohlmann1, Stefan Bruckner1, Armin Kanitsar2, Meister Eduard Gröller1
1 Vienna University of Technology
2 AGFA HealthCare

## Slide 2: Slice View Slice View

## Slide 3: 3D View Slice View
3D point deduced from viewport specification
  Rather easy to implement
  Few degrees of freedom

## Slide 4: Slice View 3D View
Much more degrees of freedom
  Viewpoint
  Clipping plane
  Zoom
?

## Slide 5: Traditional Workflow

## Slide 6: LiveSync Workflow

## Slide 7: LiveSync Workflow
Initial Views
View Input Parameters
Viewing Sphere Manipulations
Derived Viewport Parameters
Live-Synchronized 3D View

## Slide 8: LiveSync Workflow
Initial Views
View Input Parameters
Viewing Sphere Manipulations
Derived Viewport Parameters
Live-Synchronized 3D View

## Slide 9: Input Parameters
Factors to achieve live synchronization:
  Picked point
  Slice view zoom
  Patient orientation
  Local shape estimation
  Visibility
  Viewpoint history
Deformation of viewing spheres (3-6)

## Slide 10: Viewing Sphere
Concept
  Surrounds object
  Viewpoints on surface of viewing sphere
  Viewing direction to sphere’s center
Encoding of viewpoint quality
  Deformation of viewing sphere
  High radial distance indicates good viewpoint

## Slide 11: Viewing Sphere
Concept
  Surrounds object
  Viewpoints on surface of viewing sphere
  Viewing direction to sphere’s center
Encoding of viewpoint quality
  Deformation of viewing sphere
  High radial distance indicates good viewpoint
good
bad

## Slide 12: Patient-Orientation Viewing-Sphere
Consider preferred viewing directions according to type of examination
Technique: Head-feet axis serves as rough estimation to derive preferred viewpoints

## Slide 13: Local Shape-Estimation Viewing-Sphere
Consider local shape of structure of interest
Technique:
  Local region growing (picked point as seed)
  Principal component analysis on result

## Slide 14: Visibility Viewing-Sphere
Include information about occlusion
Technique: Cast & analyze visibility rays
  Exit of tissue of interest
  Distance to occluding objects

## Slide 15: Viewpoint-History Viewing-Sphere
Avoid big shifts for successive pickings
Technique: Consider previous viewpoint for estimation of current viewpoint
Candidate
Previous viewpoint
Preferred viewpoint

## Slide 16: LiveSync Workflow
Initial Views
View Input Parameters
Viewing Sphere Manipulations
Derived Viewport Parameters
Live-Synchronized 3D View

## Slide 17: Viewing-Spheres Combination
Unified representation of parameters
Each deformed sphere contains incomplete information Combination
Summation:
▪ intuitive approach
▪ good results
Multiplication:
▪ emphasize characteristics
▪ high impact of low values
Thresholding:
▪ preferred sphere
▪ definition of knock-out criteria
+
*
T

## Slide 18: Derived Viewport Parameters
Viewpoint: Indicated by highest radial distance on deformed viewing sphere
Clipping Plane: Information obtained by visibility calculation ▪ unobstructed view of picked object ▪ preservation of context information
Zoom Factor: Slice view zoom as rough estimation about size of interesting structure

## Slide 19: LiveSync Workflow
Initial Views
View Input Parameters
Viewing Sphere Manipulations
Derived Viewport Parameters
Live-Synchronized 3D View

## Slide 20: Results
Interactive live synchronization
Informal evaluation with experienced radiology technician
  No prior experience with LiveSync
  Generation of diagnostically relevant volume renderings of pathologies
  Significant speed-up with LiveSync support
Positive feedback from radiologists during demonstrations

## Slide 21: Results
Aneurism
Manual adjusted (~ 1:50 min)
LiveSync generated (< 1 sec)

## Slide 22: Results
Aneurism
LiveSync generated & manual clipping (< 20 sec)
Manual adjusted (~ 1:50 min)

## Slide 23: Results
Colon polyp
Manual adjusted (~ 4:00 min)
LiveSync support (~ 1:30 min)

## Slide 24: Results
Clips on vessel
Manual adjusted (~ 4:00 min)
LiveSync support (~ 1:00 min)

## Slide 25: Conclusion
Novel concept for live synchronization of 2D slices and volumetric view
Estimation of viewpoint quality considering different input parameters
Minimal additional user interaction
LiveSync might considerably improve the efficiency of diagnosis in clinical routine

## Slide 26: Thank you for your attention!

## Slide 27: Thank you for your attention!